## Slide 1: GPUs
CS 161: Lecture 21
4/22/2020

## Slide 2: Outline
Trends in Hardware Design
The GPU programming model
Types of GPUs
Case study: Intel’s Iris GPU

## Slide 3: Trends in Hardware Design
Bit-level parallelism: Increasing the size of instruction arguments (e.g., 32 bits  64 bits)
Instruction-level parallelism: In a single thread, allow unrelated instructions to execute in parallel
Thread-level parallelism: Giving multiple cores to a single machine
Data-level parallelism: Concurrently performing the same operation on multiple pieces of data (e.g., GPUs!)
mov (%rax), %rbx
add %rbx, %rcx
sub %r9, %r10
Must be executed in order due to the data dependency
Can be executed before, after, or between the mov+add
Notes: [Ref: “Accelerator-level Parallelism” by Hill and Reddi (https://arxiv.org/pdf/1907.02064.pdf)
https://www.eetasia.com/18083002-a-look-at-apples-vertical-integration/
]

## Slide 4: ALLOW ME TO READ SOME PAPER TEXT TO YOU

## Slide 5
Integrated Design Is What Makes The iPhone Skinny!

## Slide 6
Steve Jobs in 2007, during the launch of the first iPhone
Helped to invent object-oriented programming and window-based GUIs!
Notes: [Ref: https://www.youtube.com/watch?v=XAfTXYa36f4]

## Slide 7: Outline
Trends in Hardware Design
The GPU programming model
Types of GPUs
Case study: Intel’s Iris GPU

## Slide 8: GPUs: Overview
GPU hardware is specialized for highly-parallel, computationally-bound applications with simple control flows
The CPU offloads graphics computations to the GPU, and runs general-purpose code in parallel as the GPU works
Cache
DRAM
Control
ALU
ALU
ALU
ALU
CPU
DRAM
GPU
CPU
Launch GPU threads
GPU
Threads complete
Threads complete
Launch GPU threads
Doesn’t implement fancy stuff like out-of-order execution or branch prediction
Notes: [Ref: https://web.cs.ucdavis.edu/~amenta/f15/amenta-cuda.pdf
https://en.wikipedia.org/wiki/Single_instruction,_multiple_threads
]

## Slide 9: Maximizing Parallelization: SIMD vs. SIMT
SIMD (“single instruction, multiple data”) increases the number of calculations that are performed by one instruction
Starting in 2006, Intel has added a variety of SIMD instructions to accelerate scientific, multimedia, and cryptographic workloads
  %xmm0—%xmm15 are 128-bit registers for use by SIMD instructions
  An %xmm register is treated differently by different SIMD instructions, e.g., as
    Two 64-bit floats
    Four 32-bit floats
    Eight 16-bit shorts
    Sixteen 8-bit bytes
  Example: vector addition
//C code
vec_out.w = v1.w + v2.w;
vec_out.x = v1.x + v2.x;
vec_out.y = v1.y + v2.y;
vec_out.z = v1.z + v2.z;
movaps (v1), %xmm0 //%xmm0 = v1.z | v1.y |
// v1.x | v1.w
addps (v2), %xmm0 //%xmm0 = v1.z+v2.z |
// v1.y+v2.y |
// v1.x+v2.x |
// v1.w+v2.w
movaps %xmm0, (vec_out)
Notes: `movaps` stands for “move aligned packed single precision” floating-point values. `addps` stands for “add packed single precision” floating-point values.
[Ref: https://en.wikipedia.org/wiki/Streaming_SIMD_Extensions
https://www.felixcloutier.com/x86/movaps
https://www.felixcloutier.com/x86/addps
]

## Slide 10: Maximizing Parallelization: SIMD vs. SIMT
A “kernel” refers to a set of mathematical operations to perform—not to an OS kernel!
SIMD (“single instruction, multiple data”) increases the number of calculations that are performed by one instruction
SIMT (“single instruction, multiple threads”) is used by GPUs to increase parallelism
  Thread: A sequence of scalar (i.e., non-SIMD) instructions
  Block: A group of multiple threads where each thread:
    Contains the same instruction sequence
    Runs on the same streaming multiprocessor (SM)
    Knows its thread id and block id
    Has separate registers and local variables!
  Grid: A collection of blocks that belong to the same computational “kernel”
  Warp: A subset of threads in a block (32 on Nvidia GPUs) that simultaneously execute on the same SM
instr0
instr1
instr2
instr3
instr4
Thread instructions
Structure of a kernel
Thread
Grid
Block
Notes: Note that the grid layout is a convenient abstraction for graphics problems, since you can divide the screen into a grid, and then assign different threads to render different parts of the screen in parallel. The grid layout is also a convenient abstraction for many kinds of problems in machine learning, where training a model can be decomposed into a bunch of parallel tasks.
[Ref: https://nyu-cds.github.io/python-gpu/02-cuda/
https://en.wikipedia.org/wiki/Thread_block_(CUDA_programming)
https://en.wikipedia.org/wiki/Thread_block_(CUDA_programming)#Warps
]

## Slide 11
instr0
instr1
instr2
instr3
instr4
Thread instructions
Thread
Block
Grid
Structure of a kernel
Warp0
Warp1
Warp0
Warp7
Warp2
Warp queue
SM scheduler logic
Writeback
D-Cache
Fetch
Decode
Registers
All threads hit in D-cache
All data arrives
Warp1
Warp3
At least one thread misses
Inside a streaming multiprocessor
Notes: Note that the execute stage has enough ALUs to execute every instruction in a warp in parallel!

## Slide 12
Warp0
Warp7
Warp2
Warp queue
SM scheduler logic
Writeback
D-Cache
Fetch
Decode
Registers
All threads hit in D-cache
All data arrives
Warp1
Warp3
At least one thread misses
Inside a streaming multiprocessor
This part is similar to a traditional SIMD pipeline
  However, there are multiple threads executing the same instruction on different inputs, not one instruction operating on multiple inputs
  In SIMT, what happens if . . .
    The instruction to execute is a branch, and
    Different threads evaluate the branch condition differently?

## Slide 13: There Is A (Janky) Solution!
UGGGGGHGHHHHHHHHHHGHGHKJ
All threads in a warp execute the branch test at the same time
  The “test succeeds” threads then execute the if-path while the other threads in the warp are idle
  Afterwards, the “test fails” threads execute the else-path while the other threads in the warp are idle
So, the two execution paths execute serially!
in[] = {4,8,12}; //1D
//global input array
0: i = in[threadIdx.x];
//Thread offset in
//the 1D input data
1: if(i < 10)
2: r = 0;
else
3: r = 1;
4: out[threadIdx.x] = r;
0
T0
T1
T2
1
T0
T1
T2
4
T0
T1
T2
2
T0
T1
T2
3
T0
T1
T2
SM execution of the warp
Notes: Note that the “number:” stuff wouldn’t appear in the actual source code: those annotations just provide line numbers for the example. Also note that, in this example, `in` and `out` are global variables that are visible to all threads; in contrast, `i` and `r` are thread-local variables.
[Ref: https://cvw.cac.cornell.edu/GPU/thread_div
https://devblogs.nvidia.com/easy-introduction-cuda-c-and-c/
https://cs.calvin.edu/courses/cs/374/CUDA/CUDA-Thread-Indexing-Cheatsheet.pdf
]

## Slide 14: TRY TO AVOID BRANCHES IN GPU CODE
Notes: Branches hurt performance because they prevent the SIMD pipeline inside each SM from being fully utilized every clock cycles!

## Slide 15: Thread-Accessible Memory (Nvidia-style External GPU)
Global memory
  Visible to all threads in the application
  Persists for as long as the application runs
Local memory
  Only visible to a thread
  Only persists for the lifetime of the thread
  Bytes are actually stored in global memory!
Shared memory
  Visible to all threads in a block
  Only persists for the lifetime of the block
  Bytes typically live in per-SM RAM (e.g., 64 KB)
  Allows threads in the block to communicate with each other
Developers annotate variables (e.g., as __shared__) and the compiler (e.g., the CUDA compiler for Nvidia GPUs) is responsible for generating the right kind of memory accesses to variables
Writeback
D-Cache
Fetch
Decode
Shared memory
SM
Writeback
D-Cache
Fetch
Decode
Shared memory
SM
Global memory
GPU
Notes: [Nvidia uses the term “CUDA core” to refer to an SM.]
[Ref: https://jhui.github.io/2017/03/06/CUDA/
https://www.microway.com/hpc-tech-tips/gpu-memory-types-performance-comparison/
https://developer.download.nvidia.com/CUDA/training/register_spilling.pdf
]

## Slide 16
A single CUDA core has a warp width in the dozens (e.g., 32)!
PCIe v3.0 x16: 32 GB/s
Notes: The Titan is sold out at traditional outlets like Amazon and NewEgg. Now the only places to get it are from resellers.
[Ref: https://gist.github.com/cavinsmith/ed92fee35d44ef91e09eaa8775e3284e
https://en.wikipedia.org/wiki/PCI_Express#History_and_revisions //Provides PCIe bandwidths. Remember that
//a PCIe lane is a full-duplex connection. So, the 32 GB/s of PCIe v3.0 x16 lanes means
//16 GB/s in both directions.
https://www.pcgamer.com/nvidia-geforce-rtx-2070-super-review/
]

## Slide 17
Nvidia GeForce RTX 2070
(2560 cores, PCIe v3.0 x16)
A GPU FOR PEASANTS

## Slide 18
Notes: [Ref: https://devblogs.nvidia.com/even-easier-introduction-cuda/]

## Slide 19: Goal: Do a Vector-Addition of Two Large Arrays

## Slide 20: Version 1: Regular C++ Code
//Vector-add two arrays.
void add(int n, float *x, float *y){
for (int i = 0; i < n; i++)
y[i] = x[i] + y[i];
}
int main(){
int N = 1<<20; // 1M elements
float *x = new float[N];
float *y = new float[N];
//Initialize the arrays.
for (int i = 0; i < N; i++) {
x[i] = 1.0f;
y[i] = 2.0f;
}
//Run kernel.
add(N, x, y);
delete [] x;
delete [] y;
return 0;
}

## Slide 21: Version 2: CUDA (1 block with 256 threads)
//Vector-add two arrays.
__global__ //Tells CUDA that add()
//is a kernel that runs
//on GPU, and can be
//called by CPU.
void add(int n, float *x, float *y){
int index = threadIdx.x; //Index of the
//current thread in the block.
int stride = blockDim.x; //Total number
//of threads in block.
for (int i = index; i < n; i += stride)
y[i] = x[i] + y[i];
}
int main(){
int N = 1<<20; // 1M elements
//Allocate "unified memory" that's
//accessible from both CPU and GPU.
float *x, *y;
cudaMallocManaged(&x, N*sizeof(float));
cudaMallocManaged(&y, N*sizeof(float));
//Initialize the arrays.
for (int i = 0; i < N; i++) {
x[i] = 1.0f; y[i] = 2.0f;
}
//Run kernel (1 block and 256 threads)
add<<<1, 256>>>(N, x, y);
//Wait for GPU to finish.
cudaDeviceSynchronize();
cudaFree(x); cudaFree(y); return 0;
}

## Slide 22: Version 3: CUDA (4096 blocks, each with 256 threads)
//Vector-add two arrays.
__global__ //Tells CUDA that add()
//is a kernel that runs
//on GPU, and can be
//called by CPU.
void add(int n, float *x, float *y){
int index = (blockIdx.x * blockDim.x) +
threadIdx.x;
//(myBlockId * threadsInBlock) +
//(myThreadIdInBlock)
int stride = blockDim.x * gridDim.x;
//threadsInBlock * blocksInGrid
for (int i = index; i < n; i += stride)
y[i] = x[i] + y[i];
}
int main(){
int N = 1<<20; // 1M elements
//Allocate "unified memory" that's
//accessible from both CPU and GPU.
float *x, *y;
cudaMallocManaged(&x, N*sizeof(float));
cudaMallocManaged(&y, N*sizeof(float));
//Initialize the arrays.
for (int i = 0; i < N; i++) {
x[i] = 1.0f; y[i] = 2.0f;
}
//Run kernel (4096 blocks, 256 threads
//each)
add<<<4096, 256>>>(N, x, y);
//Wait for GPU to finish.
cudaDeviceSynchronize();
cudaFree(x); cudaFree(y); return 0;
}

## Slide 23: Performance Results (Laptop GeForce GT 750M)
Version 1 (regular C++ code): Hundreds of milliseconds
Version 2 (CUDA: 1 block, 256 threads per block): 3.2 ms
Version 3 (CUDA: 4096 blocks, 256 threads per block): 0.68 ms

## Slide 24: Outline
Trends in Hardware Design
The GPU programming model
Types of GPUs
Case study: Intel’s Iris GPU

## Slide 25: Memory-mapped PCI-e Devices
CPU package
Microway’s Octoputer
(optimized for 8 GPUs)
10 Gbps
PCI-e NIC
x4
PCH
x4
Slot6
DMI
DMI
SDRAM
RAM
x16
x16
x16
PCI-e
port 1
(x8)
PCI-e
port 2
(x16)
PCI-e
port 3
(x16)
PCI-e
switch
PCI-e
switch
x16
x8
Slot1
Slot2
Slot3
Slot4
Slot5
Root complex
x16
x16
x16
PCI-e
port 1
(x8)
PCI-e
port 2
(x16)
PCI-e
port 3
(x16)
PCI-e
switch
PCI-e
switch
x16
x8
Slot11
Slot10
Slot9
Slot8
Slot7
Root complex
SDRAM
RAM
Each PCI-e device is bound to a range of memory addresses that are managed by the device (not by actually DRAM)
The root complex translates between CPU-created memory requests and PCI-e messages
  The CPU writes to device-owned memory addresses to send commands or configure the device
  A device sends a PCI-e message to the root complex to respond to a request or proactively interrupt the CPU
Notes: Note that the Octoputer has oversubscription along its PCI-e links. Oversubscription means that all devices cannot simultaneously exchange data with a CPU at full speed. For example, each of the x16 lanes coming out of a CPU are two-way oversubscripted, because each of those x16 lanes connect to a switch which talks to TWO devices, each of which has x16 lanes. Oversubscription won’t be noticed if both of those devices are rarely active at the same time.
DMI (Direct Media Interface) is just another bus protocol. At a high level, DMI is similar to PCI-e: DMI uses lanes, differential signaling, and point-to-point connections between devices.
[Why do you need two wires to send one bit? The reason is that PCI-e uses a technology called differential signaling to transmit a bit. Differential signaling requires two wires, with a bit being encoded as the difference in the voltage between the two wires. Ref: https://en.wikipedia.org/wiki/Differential_signaling]]
[Ref: https://www.microway.com/hpc-tech-tips/pci-express-root-complex-confusion/ //The reference for the
//diagram in the slides
https://en.wikipedia.org/wiki/Direct_Media_Interface
https://en.wikipedia.org/wiki/Synchronous_dynamic_random-access_memory
]

## Slide 26: Integrated vs Discrete GPUs
An integrated GPU:
  Lives on the same package that contains the CPUs
  Communicates with the CPUs via an on-chip bus (e.g., an AGP, PCI-e, or proprietary bus that connects directly to a root complex)
A discrete GPU:
  Is a separate piece of silicon
  Communicates with the CPUs via an external bus (e.g., PCI-e lanes which connect to CPUs via a root complex)
Integrated GPUs:
  Require less space and consume less energy (due to co-design with the rest of the chip)
  Are financially cheaper
  Have worse compute performance—a discrete GPU has more space for more compute elements, and often has its own RAM and caching hierarchy
  Can access host RAM directly, avoiding copies between host RAM and GPU RAM

## Slide 27: Outline
Trends in Hardware Design
The GPU programming model
Types of GPUs
Case study: Intel’s Iris GPU

## Slide 28: Case Study: Intel’s Iris Integrated GPU
Notes: [Ref: https://software.intel.com/sites/default/files/managed/c5/9a/The-Compute-Architecture-of-Intel-Processor-Graphics-Gen9-v1d0.pdf]

## Slide 29: Case Study: Intel’s Iris Integrated GPU
Root complex
“System on a Chip”
(SoC)
L3 cache shard
L3 cache shard
PCI-e lanes
(xWhatever)
RAM
SDRAM
PCI-e device
L1-i
L1-d
L2
L1-i
L1-d
L2
Ring bus
(proprietary protocol)
Notes: The Iris is not a smartphone GPU—instead, it’s intended for laptops and desktops.
As described by Intel, in a SoC, “each on-die core is allocated a slice of cache, and that cache slice is connected as a unique agent on the ring. However, all of the slices work together as a single cache, albeit a shared and distributed cache. An address hashing scheme routes data requests to the cache slice assigned to its address. This distributed LLC is also shared with Intel processor graphics. For both CPU cores and for Intel processor graphics, LLC seeks to reduce apparent latency to system DRAM and to provide higher effective bandwidth.”
[Ref: See https://github.com/Igalia/intel-osrc-gfx-prm/tree/master/011_kbl_-_2016-2017 for the chapters in the Iris Programmer’s Reference Manual.
Also see Figure 2 of https://software.intel.com/sites/default/files/managed/c5/9a/The-Compute-Architecture-of-Intel-Processor-Graphics-Gen9-v1d0.pdf
See https://software.intel.com/sites/default/files/managed/db/88/The-Architecture-of-Intel-Processor-Graphics-Gen11_R1new.pdf; Figure 7 is
particularly relevant for the diagram above, since it depicts each core’s private L1 and L2 caches.
https://www.anandtech.com/show/3922/intels-sandy-bridge-architecture-exposed/4
]

## Slide 30: Case Study: Intel’s Iris Integrated GPU
Root complex
“System on a Chip”
(SoC)
L3 cache shard
L3 cache shard
PCI-e lanes
(xWhatever)
RAM
SDRAM
PCI-e device
Ring bus
(proprietary protocol)
L1-i
L1-d
L2
L1-i
L1-d
L2
CPU sends commands to GPU (via MMIO registers), and GPU sends interrupts to CPU, via the ring, without leaving the SoC!

## Slide 31: Case Study: Intel’s Iris Integrated GPU
“System on a Chip”
(SoC)
L3 cache shard
L3 cache shard
PCI-e lanes
(xWhatever)
RAM
SDRAM
PCI-e device
L1-i
L1-d
L2
L1-i
L1-d
L2
Ring bus
(proprietary protocol)
Root complex
GPU can access host RAM directly, without having to copy graphics buffers between on-GPU RAM and host RAM!

## Slide 32
An EU (“Execution Unit”) is an SM
  Each EU contains two SIMD ALUs
  Each ALU can issue four 32-bit operations per cycle, or eight 16-bit operations per cycle
Each sub-slice contains:
  Eight EUs
  A scheduler which assigns warps to EUs
  SLM (“Shared Local Memory”): 64 KB
The GPU has:
  Eight sub-slices (and thus 64 total EUs)
  A private L1/L2/L3 cache
  Global thread memory lives in normal system RAM, and the GPU shares the normal L3 cache with the CPUs
GTI (“Graphics Technology Interface”) is the bus interface that connects the GPU to the rest of the SoC
GTX TITAN Z:
5760 SMs
Intel Iris:
64 SMs

## Slide 33: Summary
Warp0
Warp7
Warp2
Warp queue
SM scheduler logic
Writeback
D-Cache
Fetch
Decode
Registers
All threads hit in D-cache
All data arrives
Warp1
Warp3
At least one thread misses
Challenges in semiconductor physics mean that future performance gains will likely require specialized hardware accelerators
GPUs accelerate highly-parallel, compute-bound workloads
  SM (“streaming multiprocessors”) execute the same instruction from multiple threads on different data
  Branches are handled by serializing the taken and not-taken paths
Integrated GPUs have different strengths and weaknesses than external GPUs