## Slide 1: Virtual Memory
CS 161: Lecture 3
1/29/2024

## Slide 2: Virtual Addresses
Virtual addresses are the addresses that programs manipulate
Roughly speaking, a process’ address space ranges from . . .
  Byte 0 to byte (232-1) on a 32-bit system (e.g., x86-32, PowerPC-32)
  Byte 0 to byte (264-1) on a 64-bit system (e.g., x86-64, RISC-V-64, ARMv8-A)
void main(){
int x = 42;
void* ptr = malloc(64);
printf(“&x: %p\n”, (void*)&x); //0x0000’7ffd’754e’adbc
printf(“&ptr: %p\n”, (void*)&ptr); //0x0000’7ffd’754e’adc0
printf(“ptr: %p\n”, (void*)ptr); //0x0000’5557’e367’d260
printf(“main: %p\n”, (void*)main); //0x0000’5557’e2b8’3155
}
Notes: [Note that, if you run the sample program above, you will almost certainly get different outputs than what the slide is showing. In other words, you’ll see that the various pieces of program state live in different places in virtual memory. The reason is that the OS is using a technique called ASLR (address space layout randomization) to determine, at program launch time, where exactly the stack, heap, code, and data should be located within the virtual address space.]
[Aside: RISC-V comes in 32-bit, 64-bit, and 128-bit flavors. PowerPC and MIPS also support a 64-bit mode.]

## Slide 3: How Do We Map Virtual Addresses to Physical Addresses?
0000’0000’0000’0000
FFFF’FFFF’FFFF’FFFF
64-bit virtual address
space (16 exabytes)
Physical RAM
(e.g., 8 GB)
1’FFFF’FFFF
0’0000’0000
An exabyte is a billion GBs!

## Slide 4: Memory-mapping Units (MMUs)
MMU: A piece of hardware (only configurable by privileged code) that translates virtual addresses to physical addresses
  Virtual addresses are the addresses that are generated by a running program
  Physical addresses are what a processor presents to the actual RAM
//Code in address space
subq %rax, %rbx
addq %rcx, %rdx
movq 8(%r12), %r13
MMU
Physical
RAM
VirtAddr: 0000’4d0a’fc42’9280
PhysAddr: 0xd089’5cb0

## Slide 5: Memory-mapping Units (MMUs)
MMU: A piece of hardware (only configurable by privileged code) that translates virtual addresses to physical addresses
  Virtual addresses are the addresses that are generated by a running program
  Physical addresses are what a processor presents to the actual RAM
//Code in address space
subq %rax, %rbx
addq %rcx, %rdx
movq 8(%r12), %r13
b (“byte”): one byte
w (“word”): two bytes
l (“long”): four bytes
q (“quad word”): eight bytes
VirtAddr: 0000’4d0a’fc42’9280

## Slide 6: Memory-mapping Units (MMUs)
Using indirection via the MMU:
  A virtual address space can be larger than physical RAM (and vice versa)
  At any moment, some/none/all of a virtual address space can be mapped into physical RAM
  After a context switch to a new address space, the OS can lazily bring in the non-resident memory regions as the address space’s code tries to access those regions
Physical RAM
Swap device
Virtual address
space 1
Virtual address
space 1

## Slide 7: Memory-mapping Units (MMUs)
  Protection by default: the OS maps the same virtual address in two different processes to different physical addresses
  Sharing when appropriate: a single region of physical RAM can map to multiple virtual address spaces (in possibly different virtual-memory locations!)
Isolation properties
Physical RAM
Virtual address
space 1
Virtual address
space 2
Physical RAM
Virtual address
space 1
Virtual address
space 2

## Slide 8: Outline
The structure of a virtual address space
Supporting virtual memory using paging
Fast translation using TLBs
Notes: [We didn’t have enough time to discuss TLBs in class, but the associated concepts are pretty straightforward, so students can look at the slides after lecture.]

## Slide 9: x86-64: Virtual Address Spaces
Until very recently, x86-64 chips only use 48 bits of an address
  Bits 48—63 must be copies of bit 47
  Kernel code+data lives in “high canonical” memory
  User code+data lives in “low canonical” memory
The most recent Intel chips extend addresses to 57 bits!
0000’0000’0000’0000
0000’7FFF’FFFF’FFFF
FFFF’8000’0000’0000
FFFF’FFFF’FFFF’FFFF
Virtual address space
High canonical
(kernel-only access)
Low canonical
(kernel+user access)
Physical memory map
Stack
Code
Static data
Heap
Kernel heap+stacks
Kernel code
Kernel static data
Empty gap
Notes: Why does the diagram say “kernel stacks” plural? Well, the way that Chickadee (and Linux) works is that, when a new process is allocated, that process gets a user-mode stack and a kernel-mode stack. The kernel-mode stack is empty when the user-mode code is executing, but when the kernel needs to handle a syscall on behalf of the process, the kernel code uses the kernel-mode stack of the process. [In Chickadee, a process’ kernel stack is the top half of the process’ struct proc; the struct proc is allocate an entire memory page, even though the members of the struct require much less space, so the remaining bytes in the page can be used for the kernel stack.]
[Refs: [1] https://en.wikipedia.org/wiki/X86-64#Virtual_address_space_details
[2] https://www.kernel.org/doc/Documentation/x86/x86_64/mm.txt
[3] https://www.kernel.org/doc/Documentation/x86/kernel-stacks
[4] https://jasoncc.github.io/kernel/jasonc-mm-x86.html
[5] https://notes.shichao.io/lkd/ch12/]

## Slide 10: x86-64: Virtual Address Spaces
Each process gets its own address space
  The kernel is mapped into the same place in each address space
  Content in low canonical memory is mostly unique (i.e., per-process)
Why can’t user-level code tamper with kernel state?
  The CPU’s current privilege level (CPL) indicates whether the code that is running right now is kernel code or user code
  MMU prevents unprivileged code from touching privileged memory
  The CPL flips upon user/kernel transitions (e.g., system calls)
0000’0000’0000’0000
0000’7FFF’FFFF’FFFF
FFFF’8000’0000’0000
FFFF’FFFF’FFFF’FFFF
Virtual address space
High canonical
(kernel-only access)
Low canonical
(kernel+user access)
Physical memory map
Stack
Code
Static data
Heap
Kernel heap+stacks
Kernel code
Kernel static data
Empty gap
void main(){
int x = 42;
void* ptr = malloc(64);
printf(“&x: %p\n”, (void*)&x); //0x0000’7ffd’754e’adbc
printf(“&ptr: %p\n”, (void*)&ptr); //0x0000’7ffd’754e’adc0
printf(“ptr: %p\n”, (void*)ptr); //0x0000’5557’e367’d260
printf(“main: %p\n”, (void*)main); //0x0000’5557’e2b8’3155
}
Notes: Why is the content in the bottom half of an address space only “mostly” unique? Here’s one example: suppose that you launch two different instances of a web server, so that you have two separate processes. Each process will have the same contents in its code region. However, the stacks and the heaps will be different, because each process has its own set of dynamic state that is created in response to client requests.

## Slide 11: x86-64: Virtual Address Spaces
0000’0000’0000’0000
0000’7FFF’FFFF’FFFF
FFFF’8000’0000’0000
FFFF’FFFF’FFFF’FFFF
Virtual address space
High canonical
(kernel-only access)
Low canonical
(kernel+user access)
Physical memory map
Stack
Code
Static data
Heap
Kernel heap+stacks
Kernel code
Kernel static data
Empty gap
Physical RAM
0
MAX_PHYS
Typically much smaller than the virtual address space!
Direct linear translation:
Physical address P ↔ 0xFFFF'8000'0000'0000+P
High canonical address

## Slide 12
Physical RAM
MAX_PHYS
Highest 2GB
Typically much smaller than the virtual address space!
Lowest 2GB
0x7FFF'FFFF
0
Direct linear translation:
Physical address P (0≤P≤0x7FFF'FFFF) ↔
0xFFFF'FFFF'8000'0000+P
Notes: The code and static data of the kernel are often collectively referred to as the “kernel text.”

## Slide 13
Physical RAM
0
MAX_PHYS
Typically much smaller than the virtual address space!
No simple correspondence between user-mode virtual addresses and the underlying physical addresses: the miracle of paging!
Kernel text
Wherever kernel text actually stops
Notes: Note that the actual size of the kernel text will typically be less than 2 GB in practice. In other words, it’s unlikely that an OS will have 2 GB of code and static data. So, in practice, the user-related content (e.g., like user-mode stacks) may be mapped into physical region beneath the 2GB barrier.

## Slide 14: Outline
The structure of a virtual address space
Supporting virtual memory using paging
Fast translation using TLBs

## Slide 15: Paging
MMU
V bits
Virtual Page Number
Offset
Virtual address
P bits
Physical Page Number
Offset
Physical address
Divide virtual address space and the physical RAM into fixed-sized chunks called pages
Make each page small (e.g., 4 KB)
  Good: Can allocate virtual address space with fine granularity
  Good: Only need to bring the specific pages that process needs into physical RAM
  Possibly concerning: Bookkeeping overhead—a single address space contains many pages!
Virtual address
space of V pages
Z
Y
X
Physical RAM
with P pages
X
Z
Y
MMU
Not present in RAM
(e.g., swapped to disk)
O bits
Notes: Why would a virtual page be swapped to disk? Well, there may be a lot of processes that are running; if so, that means that a lot of processes will want to put their virtual pages in RAM. If all of the pages can’t fit at once, then some of those pages need to be stored on disk, where they can be retrieved later.
Note that a virtual page may also be absent in RAM for another reason---the associated process hasn’t allocated that page. For example, the heap grows when a program calls malloc() or new. When a process initially starts, the process hasn’t allocated any heap memory, so the associated parts of the virtual address space are not associated with actual virtual pages.

## Slide 16: Paging
MMU
V bits
Virtual Page Number
Offset
Virtual address
P bits
Physical Page Number
Offset
Physical address
Make each page big (e.g., 1 GB)
  Good: Minimizes bookkeeping overhead (i.e., number of VPN->PPN mappings)
  Good/bad: Only appropriate for applications that manage huge pieces of contiguous memory (e.g., databases)
  Bad: A huge page is painful to swap to/from disk—it’s like writing or writing a 1 GB file!
x86-64 supports multiple page sizes
  4 KB
  2 MB
  1 GB
A single address space may contain
pages of different sizes
O bits

## Slide 17: Case study: x86-64
L2
L1
Offset
0
11
12
20
21
38
%cr3
L3
39
47
L4
29
30
Highest-order bits not useful for address translations!
Holds the physical address of a 4 KB-aligned PML4
Notes: “PML4” stands for “Page Map Level 4.”
[Reference: https://wiki.osdev.org/CPU_Registers_x86-64#CR3
Section 4.5 of “Intel® 64 and IA-32 Architectures Software Developer’s Manual
Volume 3 (3A, 3B, 3C & 3D): System Programming Guide
https://software.intel.com/sites/default/files/managed/2b/80/5-level_paging_white_paper.pdf
https://os.phil-opp.com/paging-introduction/
https://wiki.osdev.org/Page_Tables#Long_mode_.2864-bit.29_page_map]

## Slide 18: Case study: x86-64
PML4E
Page map level 4
9 bits
L2
L1
Offset
0
11
12
20
21
38
%cr3
L3
39
47
L4
29
30
PDPTE
Page directory pointer
9 bits
0
11
12
47
48
63
4KB-aligned PDPTE physAddr
PML4E
Bookkeeping stuff
A 4 KB-aligned PML4 has 512 8-byte entries
A 4 KB-aligned PDP has 512 8-byte entries
64 bits

## Slide 19: Case study: x86-64
L2
L1
Offset
0
11
12
20
21
38
%cr3
L3
39
47
L4
29
30
Page directory pointer
PDPTE
9 bits
PDE
Page directory
9 bits
PML4E
Page map level 4
9 bits
64 bits
0
11
12
47
48
63
4KB-aligned PDE physAddr
PDPTE
Bookkeeping stuff
A 4 KB-aligned PDP has 512 8-byte entries
A 4 KB-aligned PD has 512 8-byte entries

## Slide 20: Case study: x86-64
L2
L1
Offset
0
11
12
20
21
38
%cr3
L3
39
47
L4
29
30
Page directory pointer
PDPTE
9 bits
PDE
Page directory
9 bits
PML4E
Page map level 4
9 bits
64 bits
A 4 KB-aligned PD has 512 8-byte entries
0
11
12
47
48
63
4KB-aligned PTE physAddr
PDE
Bookkeeping stuff

## Slide 21: Case study: x86-64
L2
L1
Offset
0
11
12
20
21
38
PTE
9 bits
%cr3
Page table
L3
39
47
L4
29
30
PhysAddr
12 bits
4KB page
PDE
Page directory
9 bits
PDPTE
Page directory pointer
9 bits
PML4E
Page map level 4
9 bits
64 bits
0
1
2
3
11
12
47
48
63
4KB-aligned physFrame addr
PTE
Present?
Writeable?
User-mode accessible?
A 4 KB-aligned PT has 512 8-byte entries
Notes: [Quoth Eddie’s 2018 lecture notes: “Question: Why does each index get 9 bits? Answer: Because the size of one page is 2^12 bytes, and each page table page entry is an address which has 2^3 bytes. 212/23 = 2^9 entries per page. We want to be able to index into any given entry, which means we need 9 bits.”]

## Slide 22: Why so many levels?
Virtual address spaces are sparse!
  Ex: Most processes don’t have gigabytes of code
  Ex: Most processes don’t have gigabytes of stack frames
Multi-level tables: only materialize entries for live parts of address space
  Ex: A single PML4E covers 512 GB
  If none of those addresses are in use, just set the PML4E.present bit to 0!
  Don’t need to create PDP/PD/PT tables for the subtree
0
11
12
47
48
63
4KB-aligned PDPTE physAddr
PML4E
Bookkeeping stuff
0
1
2
3
11
12
47
48
63
4KB-aligned PDPTE physAddr
Present?
Writeable?
User-mode accessible?
PML4E
Bookkeeping stuff

## Slide 23: Case study: x86-64 using 1 GB pages
PML4E
Page map level 4
9 bits
%cr3
PDPTE
Page directory pointer
9 bits
Offset in 1 GB page
0
38
L3
39
47
L4
29
30
0
11
12
47
48
63
4KB-aligned PDPTE physAddr
PML4E
Bookkeeping stuff
A 4 KB-aligned PML4 has 512 8-byte entries
A 4 KB-aligned PDP has 512 8-byte entries
64 bits

## Slide 24: Case study: x86-64 using 1 GB pages
PML4E
Page map level 4
9 bits
%cr3
PDPTE
Page directory pointer
9 bits
0
38
L3
39
47
L4
29
30
A 4 KB-aligned PDP has 512 8-byte entries
64 bits
0
11
12
47
48
63
1GB-aligned huge page physAddr
PDPTE
Bookkeeping stuff
7
PS (“Page size”) bit set to 1, indicating a 1 GB page
Offset in 1 GB page

## Slide 25: Chickadee’s Early Boot
“Booting a processor” means “configuring a processor once it’s been turned on”
Booting a processor is a delicate dance, particularly on x86!
Chickadee’s k-init.cc contains important code related to booting
init_hardware()
init_early_memory()
//Create the boot-
//time page tables
//and tell CPU to
//enable paging
init_interrupts()
//Ensure that CPU
//invokes kernel to
//handle timers,
//syscalls, etc.
init_other_processors()
//On a multi-core machine,
//ask the other cores to
//come online!

## Slide 26
Bottom 512 GB
init_early_memory()
//Create the boot-
//time page tables
//and tell CPU to
//enable paging
%cr3
64 bits
[0]
L4 pagetable
[256]
[511]
. . .
Physical RAM
[0]
L3 pagetable (ps=1GB)
[511]
. . .
[0]
L3 pagetable (ps=1GB)
[511]
. . .
[510]
. . .
. . .
Physical memory map
Notes: [Note that there are hex 1’0000’0000’0000= 262,144 GB total bytes of allowable virtual memory---half of that belongs to low-canonical memory in 0000’0000’0000’0000--0000’7FFF’FFFF’FFFF, and the other half belongs to high canonical memory in FFFF’8000’0000’0000--FFFF’FFFF’FFFF’FFFF. If an L3 pagetable has ps=1 GB, then each L3 pagetable can cover 512 GB. So, if an L4 table has 512 entries, and each entry points to an L3 page table covering 512 GB of memory, then a single L4 can cover 512 * 512 GB = 262,144 GB of memory!]

## Slide 27
Bottom 512 GB
%cr3
64 bits
[0]
L4 pagetable
[256]
[511]
. . .
Physical RAM
[0]
L3 pagetable (ps=1GB)
[511]
. . .
[0]
L3 pagetable (ps=1GB)
[511]
. . .
[510]
. . .
. . .
Physical memory map
//x86-64.h
typedef uint64_t x86_64_pageentry_t;
typedef struct x86_64_pagetable {
x86_64_pageentry_t entry[1 << PAGEINDEXBITS];
} x86_64_pagetable;
//k-init.cc
x86_64_pagetable early_pagetable[3];
early_pagetable[0]
early_pagetable[1]
early_pagetable[2]
Notes: [Aside: Chickadee's MEMSIZE_PHYSICAL is set to 0x200000 == 2MB. However, qemu is what determines the upper limit on how much memory is actually available on the emulated machine that Chickadee runs atop. By default, qemu provides 128 MB of emulated physical memory---see the discussion of the qemu -m option at https://wiki.gentoo.org/wiki/QEMU/Options. Chickadee uses the qemu default, so MEMSIZE_PHYSICAL == 0x200000 == 2MB < 128MB is saying that Chickadee actually only manages 2MB of a possible 128MB of emulated physical RAM.]

## Slide 28
Bottom 512 GB
%cr3
64 bits
[0]
L4 pagetable
[256]
[511]
. . .
Physical RAM
[0]
L3 pagetable (ps=1GB)
[511]
. . .
[0]
L3 pagetable (ps=1GB)
[511]
. . .
[510]
. . .
. . .
Physical memory map
//x86-64.h
typedef uint64_t x86_64_pageentry_t;
typedef struct x86_64_pagetable {
x86_64_pageentry_t entry[1 << PAGEINDEXBITS];
} x86_64_pagetable;
//k-init.cc
x86_64_pagetable early_pagetable[3];
early_pagetable[0]
early_pagetable[1]
early_pagetable[2]
void init_early_memory() {
//...some code, and then...
//First level-3 page table maps first
//512GiB of physical memory (low
//canonical and high canonical)
for (uintptr_t p = 0; p < 512; ++p) {
early_pagetable[1].entry[p] = (p << 30) |
PTE_P | PTE_W | PTE_PS;
}
//Second level-3 page table maps its
//last 2 slots to the first 2GiB of
//of physical memory (kernel text)
early_pagetable[2].entry[510] =
early_pagetable[1].entry[0];
early_pagetable[2].entry[511] =
early_pagetable[1].entry[1];
wrcr3(ktext2pa(early_pagetable));
}
Notes: Note that, in the excerpt of init_early_memory() that I show above, I don’t show the code that initializes the first, middle, and last entry of the L4 page table. That initialization happens in the “//…some code, and then…” part of the snippet.
[That initialization code looks like this:
// level-4 page table:
// - entry 0 maps first 512GiB of low canonical addresses
// - entry 256 maps first 512GiB of high canonical addresses
// - entry 511 maps last 2GiB of high canonical addresses (kernel text)
early_pagetable->entry[0] = ktext2pa(&early_pagetable[1]) | PTE_P | PTE_W;
early_pagetable->entry[256] = early_pagetable->entry[0];
early_pagetable->entry[511] = ktext2pa(&early_pagetable[2]) | PTE_P | PTE_W;
Here’s the definition of ktext2pa():
inline uint64_t ktext2pa(uint64_t ka) {
assert(ka >= KTEXT_BASE);
return ka - KTEXT_BASE;
}
So, ktext2pa() is just doing a direct linear translation of a kernel text virtual address (which is assumed to be in the topmost part of high canonical memory) to a physical address at the bottom of physical RAM. Remember that kernel text (i..e, kernel code and kernel static data) is mapped to the bottom of physical RAM.
]

## Slide 29: Chickadee: Page Tables
During boot, Chickadee creates a physical memory map in high canonical addresses *and* low canonical addresses
However, post-boot, low-canonical addresses are for user-mode content, not a memory map!

## Slide 30
Bottom 512 GB
%cr3
64 bits
[0]
L4 pagetable
[256]
[511]
. . .
Physical RAM
[0]
L3 pagetable (ps=1GB)
[511]
. . .
[0]
L3 pagetable (ps=1GB)
[511]
. . .
[510]
. . .
. . .
Physical memory map
//x86-64.h
typedef uint64_t x86_64_pageentry_t;
typedef struct x86_64_pagetable {
x86_64_pageentry_t entry[1 << PAGEINDEXBITS];
} x86_64_pagetable;
//k-init.cc
x86_64_pagetable early_pagetable[3];
early_pagetable[0]
early_pagetable[1]
early_pagetable[2]

## Slide 31: Chickadee: Page Tables
During boot, Chickadee creates a physical memory map in high canonical addresses *and* low canonical addresses
However, post-boot, low-canonical addresses are for user-mode content, not a memory map!
  The boot-time kernel only needs the low-canonical memory map to assist with x86 configuration horrors
  At a more detailed level, I DON’T WANT TO TALK ABOUT LOW-LEVEL X86 CONFIGURATION HORROR
  However, early_pagetable will become important in pset2!

## Slide 32: Outline
The structure of a virtual address space
Supporting virtual memory using paging
Fast translation using TLBs

## Slide 33: Paging: The Good and the Bad
Good: A virtual address space can be bigger/smaller than physical memory
Bad: Each virtual memory access now requires five physical memory accesses
x86-64 physical memory accesses
Load entry from page map level 4
Load entry from page directory pointer
Load entry from page directory
Load entry from page table
Generate the “real” memory access

## Slide 34
Does 5x overhead sound like a lot?
IT IS INDEED A LOT.

## Slide 35: Translation Lookaside Buffers (TLBs)
Idea: Cache some PTEs (i.e., V->P translations) in a small hardware buffer
  If virtual address has an entry in TLB, don’t need to go to physical memory to fetch a PTE!
  If virtual address misses in TLB, we must walk the page table to fetch a PTE
L1 d-cache
L1 i-cache
L2 cache
L3 cache
L1 d-cache
L1 i-cache
L2 cache
RAM
TLB
TLB
Key/value store: key is high bits of virt addr, value is phys frame number

## Slide 36: Translation Lookaside Buffers (TLBs)
Idea: Cache some PTEs (i.e., V->P translations) in a small hardware buffer
  If virtual address has an entry in TLB, don’t need to go to physical memory to fetch a PTE!
  If virtual address misses in TLB, we must walk the page table to fetch a PTE
TLBs are effective because programs exhibit locality
  Temporal locality
    When a process accesses virtual address x, it will likely access x again in the future
    Ex: a function’s local variable that lives on the stack
  Spatial locality
    When the process accesses something at memory location x, the process will likely access other memory locations close to x
    Ex: reading elements from an array on the heap
Notes: Temporal locality means that a TLB entry that has recently been accessed will be accessed again in the near future.
Spatial locality means that, when we access a virtual address x, and we create a TLB entry for the associated page, the TLB entry will likely be useful for other virtual addresses that the program accesses. Remember that a TLB entry covers an entire page of spatially contiguous addresses! For machines that have a lot of physical RAM, you might want a single TLB entry to cover a much larger region than 4 KB. x64 supports this idea using “superpages.” When a process’s page table uses superpages, each PTE and TLB entry covers 2 MB or 1 GB instead of 4 KB.

## Slide 37: The Lifecycle of a Memory Reference on x86
Virtual address
TLB lookup
TLB hit?
Access ok?
Found PTE for virt frame?
Yes
Calculate phys addr, send to L1/L2/L3/RAM
Check protection bits
Yes
HW raises a page fault
No
HW updates TLB
Yes
HW raises a page fault
No
HW walks the page table
No
Notes: Note that the protection bits state things like “is this page writable?” and “is this page accessible to user-mode processes?”
If there’s a TLB miss, the hardware walks the page table. If the hardware doesn’t find a valid PTE, i.e., if the PTE for the virtual address is not set to “present,” then the hardware raises a fault. Note that a fault could be raised for one of two reasons: the virtual address may reside in an unallocated part of the virtual address space (e.g., in the hole between the stack and the heap). Alternatively, the virtual address may reside in an allocated page of the address space, but that page is not in physical memory.

## Slide 38: The Lifecycle of a Memory Reference on x86
Virtual address
TLB lookup
HW walks the page table
Check protection bits
HW updates TLB
Calculate phys addr, send to L1/L2/L3/RAM
HW raises a page fault
TLB hit?
Found PTE for virt frame?
Access ok?
HW raises a page fault
Yes
No
Yes
No
No
Yes
Before raising page fault exception, HW sets %cr2 to faulting address, and pushes an error code onto stack
-Ex: User process tried to read a nnon-present page
-Ex: User process tried to write aa present but read-only page