## Slide 1: Embedded EthiCS
CS 1610
4/22/2026

## Slide 2: Linux Patches
When a kernel developer wants to patch the kernel (e.g., to fix a bug or improve performance), she has to:
  Generate a diff relative to the current kernel source
  Write an English-level description of the patch, explaining the “user-visible impact” and quantifying “optimizations and trade-offs”
  Find the maintainers for the associated kernel subsystem, and email the patch to those maintainers
Notes: [Ref: https://www.kernel.org/doc/html/v7.0/process/submitting-patches.html]

## Slide 3
Notes: “M” indicates who patches should be mailed to. “L” indicates the mailing list that is associated with a kernel subsystem.
[Ref: https://www.kernel.org/doc/linux/MAINTAINERS]

## Slide 4
Notes: [Ref: https://patchwork.kernel.org/project/qemu-devel/patch/20210416125256.2039734-1-thuth@redhat.com/]

## Slide 5: Linux Patches
When a kernel developer wants to patch the kernel (e.g., to fix a bug or improve performance), she has to:
  Generate a diff relative to the current kernel source
  Write an English-level description of the patch, explaining the “user-visible impact” and quantifying “optimizations and trade-offs”
  Find the maintainers for the associated kernel subsystem, and email the patch to those maintainers
The maintainers then test the patch and may or may not merge it into the kernel
Notes: [Ref: https://www.kernel.org/doc/html/v7.0/process/submitting-patches.html]

## Slide 6: How Do We Determine Whether a Patch is “Worth Merging”?

## Slide 7
Notes: [For a high-level overview of the attack, see Ref [1]. For a more detailed analysis, see Ref [2]. The second reference refers to the attacker leveraging “transient execution”; to understand what that term means, see Ref [3]. The next few slides in this deck simplify the discussion of the snooping attack, eliding exactly how the attacker uses transient execution to inappropriately observe data.]
[Ref: [1] https://www.zdnet.com/article/intel-cpus-vulnerable-to-new-snoop-attack/
[2] https://www.intel.com/content/www/us/en/developer/articles/technical/software-security-guidance/technical-documentation/snoop-assisted-l1-data-sampling.html
[3] https://software.intel.com/security-software-guidance/best-practices/refined-speculative-execution-terminology
]

## Slide 8: The MESI Protocol
RAM
Address: x
Data: d0
Data
Address
State
State
Address
Data
Invalid
Invalid
Invalid
d1
x
Modified
Suppose that the core on the right has a modified cache line that belongs to kernel-visible thread T0 in address space AVictim.
T0:AVictim

## Slide 9: The MESI Protocol
RAM
Address: x
Data: d0
Data
Address
State
State
Address
Data
Invalid
Invalid
Invalid
d1
x
Modified
Now suppose that the core on the right starts running a malicious thread from a different address space.
T0:AEvil
T0:AVictim
T0:AEvil should not be able to read the cache line from AVictim—the address spaces are different!

## Slide 10: The MESI Protocol
[Left CPU]
(k) Invalid to shared: CPU reads data that wasn’t in the local cache (but was in the other CPU’s cache)
RAM
Data
Address
State
State
Address
Data
Invalid
Invalid
Invalid
Address: x
Data: d0
Read x
Hey, other cache, do you have x’s data?
Yeah, here it is!
d1
x
Shared
d1
x
Modified
Shared
[Right CPU]
(g) Modified to shared: The right CPU lost its exclusive access to the data
Now suppose a new thread from the victim address space runs on the left core, and tries to read the cache line . . .
T0:AEvil
T1:AVictim

## Slide 11
Intel chips had a hardware bug that allowed T0:AEvil to “snoop” on the cache message sent from the right core to the left one, allowing T0:AEvil to read the cache line from AVictim!

## Slide 12: Patching Linux to Stop the Attack
An Amazon engineer wrote a kernel patch to address the snooping attack
  The patch added a new system call which marked the calling process as wanting to prevent the snooping attack
  When Linux context-switched away from such a process, the kernel would force the CPU to flush the cache
RAM
Address: x
Data: d0
Data
Address
State
State
Address
Data
Invalid
Invalid
Invalid
d1
x
Modified
T0:AVictim

## Slide 13: Patching Linux to Stop the Attack
An Amazon engineer wrote a kernel patch to address the snooping attack
  The patch added a new system call which marked the calling process as wanting to prevent the snooping attack
  When Linux context-switched away from such a process, the kernel would force the CPU to flush the cache
RAM
Address: x
Data: d0
Data
Address
State
State
Address
Data
Invalid
Invalid
Invalid
d1
x
Modified
T0:AEvil
Invalid
Invalid
Invalid
d1
T0:AVictim

## Slide 14
Linus
Notes: [Ref: https://lore.kernel.org/lkml/CAHk-=wgXf_wQ9zrJKv2Hy4EpEbLuqty-Cjbs2u00gm7XcYHBfw@mail.gmail.com/]

## Slide 15
Linus was trying to do a cost-benefit analysis.